# PART 1 GENERAL

## SECTION INCLUDES

### Single-sided Game Clock LED basketball scoreboard

## references

### Standard for Electric Signs, UL-48, 13th Edition

### Standard for Control Centers for Changing Message Type Signs, UL-1433, 1st Edition

### Standard for CAN/CSA C22.2 No. 207-M89 for indoor use

### Federal Communications Commission Regulation Part 15

### National Electric Code

## SUBMITTALS

### Product data: Submit manufacturer’s product illustrations, data and literature that fully describe the scoreboards and accessories proposed for installation.

### Shop drawings: Submit mechanical and electrical drawings.

### Maintenance data: Submit manufacturer’s installation, operation, and maintenance manuals.

## DELIVERY, STORAGE, AND HANDLING

### Product delivered on site.

### Scoreboard and equipment to be housed in a clean, dry environment.

## Project CONDITIONS

### Environmental Limitations: Do not install scoring equipment until spaces are enclosed and weatherproof, wet work in spaces is complete and dry, and ambient temperature and humidity conditions are maintained at the levels indicated for project when occupied for its

### intended use.

### Field Measurements: Shot clock mounting brackets supplied by the backstop provider. Provide size, weight and mounting location for coordination.

### Verify building structure is capable of supporting the scoreboard's weight in addition to the auxiliary equipment.

## quality assurance

### For indoor use only

### Source Limitations: Obtain each type of scoring equipment and electronic displays through one source from a single manufacturer.

### ETL listed to UL Standards 48 and 1433

### NEC compliant

### FCC compliant

### ETLC listed to CAN/CSA 22.2

## WARRANTY/service plan

### Provide 5 years of coverage.

### Provide an exchange program to supply replacement parts for components that fail during the coverage period. To minimize downtime, the exchange parts are shipped on the same day the order is received or on the following day. The manufacturer will also enclose an air bill for return of the defective components.

### Provide access to a local Authorized Service Company.

### Provide a help desk staffed by experience technicians and coordinators who are thoroughly familiar with the scoreboard and available for technical support. This staff must be available at no additional cost to the customer and provide an "on-call" service during weekends.

# PART 2 PRODUCTS

## manufacturer

### Eversan, Incorporated, 34 Main Street, Whitesboro, NY 13492

### ___________________________________________________________________

### ___________________________________________________________________

## Product

### Eversan, Inc. single-sided shot timer basketball scoreboard displays game and event time including 1/10 second timing during the last minute, and counts down from any preset number between 0 and 99.

## scoreboard

### General information

#### Dimensions: 2'-5" (737 mm) high, 2'-2" (660 mm) wide, 0'-6" (152 mm) deep

#### Weight: 26 lb (12 kg)

#### Power requirement: 8 W Ultra Efficient LED design

#### Color: Specified by Customer

### Construction

### All-aluminum construction.

#### Scoreboard perimeter: 0.080" thick

#### Scoreboard face and back: 0.063" thick

#### Digit faceplates: 0.063" thick

#### Finish: Powder coat finish with high performance, architectural powder coat with

#### UV protection to reduce color fading, no wet paint finish allowed

#### Cabinet with stands high-velocity impact from indoor sports balls without the need for protective screens.

### Digits

#### AS  AlInGaP LED digits

#### Seven bar segments per digit LED digit technology: A diffuser over the LEDs blends the light achieving a uniform look with 170 degrees wide viewing angle. Digit in Motion ™, italic number, technology

#### Clock digits: 6" (152 mm) high

4.	All other digits: 12" (305 mm) high

5.	All digits: red LEDs

### Horn

#### Vibrating horn: mounts behind scoreboard face

#### Sounds automatically when shot clock counts down to zero

#### Sounds manually as directed by operator

### Power Cord

#### Cord is 6' (1829 mm) long

#### Cord plugs into a standard grounded 120 V AC outlet

1.20    SCORING CONTROL CONSOLE

- Console is the 9750/60 controller

- Capable of scoring basketball, volleyball, and wrestling without changing keyboard inserts

- Capable of controlling all 9700 series scoreboards

- Console has a maximum power requirement of 5 watts

- Console includes:

- A rugged stainless steel enclosure to house electronics

- Weather resistant push button switches and keypad

- All-weather waterproof laser function label, console labels will never fade, crack, or peel

- 20 character two line liquid crystal display to verify entries and recall information currently displayed

- A 6’ (1829mm) power cord to plug into a standard 120VAC outlet

- Optional Equipment

- Carrying case for control console

- 2.4 GHz spread spectrum 200mW radio for scoreboard control in a dynamic network that requires no channel selection by the operator via the control console or through the use of dip switch on the scoreboard or control console

- 12V Battery pack with charger

- LED backboard indicator strips

- Goal light

# Part 3 EXECUTION

# 3.01  EXAMINATION

A.	Verify that surfaces scoreboard will be mounted on a ready to receive work. Verify that placement of conduit and junction boxes are as specified and indicated in plans and shop drawings.

3.02	INSTALLATION

### Power conduit, cables and outlet boxes to be provided and installed by the electrical contractor. Signal raceways conduit and boxes to be provided by the electrical contractor. Electrical contractor is responsible for pulling, signal wire and terminators between each scoreboard and control location. Scoreboard vendor to terminate signal wire of controller and conduit scoreboard.

### Mount shot clock to backstop brackets in location detailed and in accordance with manufacturer's instructions. Unit to be plumb and level.

## 3.03	installation—control center

### A.    Provide boxes, cover plates, and jacks as required to meet control specifications requirements. Control cables to control panels are concealed.

### B.    Test the operation of the scoreboard, controller and all control jacks, leave control unit in carrying case and other loose items with owner's designated representative.

### C     Conduct operator training on the scoreboard/controller operation

END OF SECTION