## PART 1 GENERAL

  - SECTION INCLUDES

- Single-sided LED Basketball Scoreboard

  - REFERENCES

- Standards for Electric Signs, UL-48, 13th Edition

- Standards for Control Centers for Changing Message Type Signs, UL-1433 1st Edition

- Standards for CAN/CSA C22.2

- Federal Communications Commission Regulation Part 15

- National Electric Code

  - SUBMITTALS

- Product data: Submit manufacture’s product illustrations, data and

literature that full describe the scoreboards and accessories proposed

for installation.

- Shop Drawings: Submit mechanical and electrical drawings

- Maintenance data: Submit manufacturer’s installation, operation, and maintenance manuals.

  - DELIVERY, STORAGE, AND HANDLING

- Product delivered on site.

- Scoreboard and equipment to be housed in a clean dry environment.

  - PROJECT CONDITIONS

- Environmental Limitations: Do not install scoring equipment until spaces are enclosed and weatherproof, wet work in spaces is complete and dry, and ambient temperature and humidity conditions are maintained at the levels indicated for project when occupied for its intended use.

- Field Measurements: Coordinate scoreboard location and height with the customer. Verify dimensions by field measurements.

- Supply weight and mounting method for owner to verify that building structure is capable of supporting the scoreboard’s weight in addition to the auxiliary equipment.

  - QUAILITY ASSURANCE

- For indoor or outdoor use.

- Source Limitations: Obtain each type of scoring equipment and electronic displays though one source.

- ETL listed to UL Standards 48 and 1433.

- NEC compliant

- FCC compliant

- ETLC listed to CAN/CSA 22.2

  - WARRANTY/SERVICE PLAN

- Provide 5 years of coverage.

- Provide an exchange program to supply replacement parts for components that fail during the coverage period. To minimize downtime, the exchange parts shall be shipped on the same day the order is received or the following day. The manufacturer will include an air bill for the return of the defective components.

- Provide a help desk staffed by experienced technicians and coordinators who are thoroughly familiar the scoreboard and available for technical support. The staff must be available at no extra cost to the customer.

## PART 2 PRODUCTS

2.01 MANUFACTURER

- Eversan, Inc., 34 Main Street, Whitesboro, NY 13492

2.02 PRODUCT

- Eversan, Inc. Model 6765 single sided LED basketball scoreboard can

also score volleyball and wrestling. It scores HOME and GUEST to 199, displays     period time to 99:59 and during the last minute of the period; it displays time to 1/10th of a second. It displays PERIOD, FOUL and T.O.L to 9 and PLAYER, and FOULS to 99. In addition it includes possession and bonus indicators.

2.03 SCOREBOARD

- General Information

- Dimensions: 7’-0” (2133mm) high, 14’-0” (4267mm) wide, 0-3.5” (89mm) deep

- Weight: 250 lbs. (113 kg)

- Power requirement: 120 VAC @ 300 W

- Color: Specified by Customer

- Construction

- All aluminum construction

- Scoreboard face, perimeter, and back: 0.080” thick

- Digit Faceplates: 0.080” thick

- Cabinet withstands high-velocity impact from indoor sports balls without need for protective screens.

#### Digits

- AS AlInGaP LED digits

- Seven bar segments per digit

- LED digit technology: Through face technology with 140 degree viewing angle. Digit in Motion ™, italic number, technology

4.    Time and score digits: 18” (457mm) high

- All remaining digits are 15” (381 mm) high

- Score and time digits and all indicators: red or amber LEDs

#### Captions

- HOME and GUEST captions: 7” (177mm) high

- All other captions 5” (127mm) high

- Striping ¾” (19mm) wide

#### Logo/Sponsor Panels

- There is a space for two 16” (406mm) high, 24” (610mm) wide

logo/sponsor panels on the top corners of the scoreboards

#### Horn

- Horn: mounts on scoreboard face

- Sounds automatically when period clock counts down to zero

- Sounds manually as directed by the operator

- Power Cords

- 1.   Cord is 6’ (1823mm) long

- Cord plugs into standard 120VAC outlet

- Optional Equipment

- Vinyl team logo/sponsor graphics

- Vinyl team name caption in place of HOME caption

- Logo/sponsor panel

- Corner sponsor/logo panel

- Programmable Team Name Message Centers

- Programmable Message Centers

- Protective Cage

- Hardware for Suspension installation

2.04 SCORING CONTROL CONSOLE

- Console is the 9750/60 controller

- Capable of scoring basketball, volleyball, and wrestling without changing keyboard inserts

- Capable of controlling all 9700 and 6700 series scoreboards

- Console has a maximum power requirement of 5 watts

- Console includes:

- A rugged stainless steel enclosure to house electronics

- Weather resistant push button switches and keypad

- 20 character two line liquid crystal display to verify entries and recall information currently displayed

- A 6’ (1829mm) power cord to plug into a standard 120VAC outlet

- Optional Equipment

- Carrying case for control console

- 2.4 GHz spread spectrum radio for scoreboard control

- 12V Battery pack with charger

PART 3 EXECUTION

3.01 EXAMINATION

- Verify surfaces that the scoreboard is to be mounted to are ready to receive the work. Verify that the conduit and junction boxes specified are as specified and indicated in the plans and shop drawings. Verify concrete has cured adequately according to specifications.

3.02 INSTALLATION

- Power conduit, cabling and outlet boxes to be provided and installed by the electrical contractor. Signal raceways conduit and boxes to be provided by the electrical contractor. Electrical contractor is responsible for pulling signal wires between each scoreboard and control console location. Scoreboard vendor to terminate signal wire of control console and scoreboard.

- Mount scoreboards and interior displays to wall in location detailed and in accordance with manufacturer’s instructions. Unit to be plumb and level.

3.03 INSTALLATION-CONTROL CONSOLE

- Provide boxes, cover plates and connectors as required to meet control specification requirements. Control cables from scoreboard to control console junction box shall be concealed.

- Test the operation of the scoreboard, control console and all cables and connections. Leave control console unit in carrying case and other loose items with owner’s designated representative.

- Conduct operator training on the scoreboard/ controller operation.

END OF SECTION